Building and Configuring the Ingex
tapeless recording software

V1.07
16/12/2008

# Installing openSUSE

These instructions apply to the 32-bit version of openSUSE 10.3.
As some of the required standard packages aren't on the installation DVD, when installing openSUSE initially, it will help if you select the option “Add Online Repositories” when you reach the page “Installation Mode” (where it indicates New Installation).
Alternatively you can add the online repository later in YaST using these details:
Protocol: http
Port: 80
Server: download.opensuse.org
Directory on server: /distribution/10.3/repo/oss/

It's also more convenient to include the following packages during installation by clicking on the heading “Software” when you reach the screen “Installation Settings”:
Server Functions
- File server
- Web and LAMP server
Development
- C/C++ development
- Perl development
- Linux Kernel Development

After installation you should remove these packages using YaST:
beagle
beagle-firefox
beagle-index
kdebase3-beagle
kio-beagle
libbeagle
kerry
As you are doing this, a conflict resolution warning will appear but this is resolved once all these packages have been removed. (We have found that Beagle can unexpectedly consume significant CPU resources and affect the recorder operation.)
Some parts of these instructions are written assuming that you are using KDE for the desktop.

# Before you start

## Set up new user
It will help to go into YaST->Security and Users -> User Management and create a new user named 'ingex' as this gives a clean area in which to work.
It's also be convenient to allow the user ingex to be able to use the “sudo” command to run commands with root privileges. You can enable this in YaST -> Security and Users ->sudo.
## Terminology
The styling used in this document is that each example command line starts with a prompt string such as ingex> which mean the command such be entered as the user ingex. The alternative is root> which means you should be root to enter this command. Remember that this prompt is not part of the command; the command starts after the '>'.
# Downloading the Ingex software

Login as user ingex, open a terminal window and start by making a local directory for the software.
ingex> mkdir ~/ap-workspace
ingex> cd ~/ap-workspace

Now download the Ingex software from the CVS respository on Sourceforge, with these two commands:
First login with this command. When prompted for a password, just press enter.
ingex> cvs -d:pserver:anonymous@ingex.cvs.sourceforge.net:/cvsroot/ingex login

Next get the ingex source code with the checkout command:
ingex> cvs -z3 -d:pserver:anonymous@ingex.cvs.sourceforge.net:/cvsroot/ingex co -P ingex

This will download the entire project.

Throughout these instructions, the term "$workspace" is used to refer to the directory into which you have just checked out the Ingex project from CVS, i.e. the directory /home/ingex/ap-workspace, above. Either just bear that in mind when typing the commands or set this as an environment variable if you wish, with this command:
ingex> export workspace=/home/ingex/ap-workspace

It would be sensible to put this line into your .bashrc file (i.e. ~/.bashrc), so it's always set.

## Troubleshooting
If the CVS download fails because you are behind a proxy server, add the proxy details to the cvs command, as in the next example, but using the IP address and port number for your proxy server:
ingex> cvs "-d:pserver;proxy=192.168.1.255;proxyport=80:anonymous@ingex.cvs.sourceforge.net:/cvsroot/ingex" login

ingex> cvs -z3 "-d:pserver;proxy=192.168.1.255;proxyport=80:anonymous@ingex.cvs.sourceforge.net:/cvsroot/ingex" co -P ingex

As an alternative to using the proxy option in the cvs command, you can instead use tsocks.

# Installation Prerequisites

There are four main sets of packages to install before building the Ingex software:
- additional standard packages supplied with the SUSE distribution
- pre-built RPMs of other packages used by Ingex
- the DVS SDK
- the AAF SDK
Not all of these are required for each part of the Ingex software, so if you wish to build the modules separately and want a minimum installation, refer to their separate build instructions.
## 1. Standard Packages
Open YaST and under Software Management, install

libuuid-devel
libjpeg-devel
libbz2-devel
unixODBC
unixODBC-devel
perl-DBD-Pg
psqlODBC
portaudio-devel
postgresql-server
Xerces-c
libpqxx (must be >= version 2.6.9)
libpqxx-devel
libXerces-c-27
libXerces-c-devel
wxGTK-devel

If you selected the software options suggested in "Installing SUSE" during installation, then the following packages should already be installed. Install them now if YaST indicates they're not present.
autoconf
automake
kernel sources
libtool
libuuid1
fontconfig-devel
freetype2-devel

## 2. Pre-built RPMs
#### i) ACE and TAO
Communications between the Ingex recorder software and its controller is implemented using ACE (the “Adaptive Communications Environment”) and TAO (“The ACE ORB”). Full details of these packages are available from www.cs.wustl.edu/~schmidt/ACE.html and extensive documentation can be found there.

The ACE and TAO software is now available as an RPM from the OpenSuse repository.
Add the repository in YaST and install the required ACE and TAO software, as follows.

Note: if you have built ACE and TAO by following previous versions of the build instructions for Ingex, then see the comment below about environment variables.
#### Adding the repository
Start YaST and select Software, then Software Repositories.

Click on “Add”, to add the new repository using these details:

Protocol: HTTP
Server Name: download.opensuse.org
Port: 80
Directory on server: /repositories/devel:/libraries:/ACE/openSUSE_10.3

Which makes the complete URL:
http://download.opensuse.org/repositories/devel:/libraries:/ACE/openSUSE_10.3/
Click on Finish to add the repository.

A warning message saying that this is signed with an untrusted key will appear. Accept this by clicking on “Trust & Import the key”.

#### Installing the ACE and TAO packages
Now the repository has been added, you can install the required ACE and TAO software by selecting Software and then Software Management in YaST, and selecting these packages:
- ace
- ace-devel
- ace-gperf
- mpc
- tao
- tao-devel
- tao-cosnaming

The following dependencies should also be installed if YaST requests them, although they are not really needed:
- ace-xml
- ace-kokyu

Click on Finish to exit YaST.
#### Previous environment variables
If you have installed Ingex previously by following an earlier version of these instructions then you will have set the environment variables ACE_ROOT, TAO_ROOT or LD_LIBRARY_PATH in your .bashrc file. These are no longer required and must be removed.

#### ii) RPM installation
To assist with the build, binary RPMs of additional packages are available from the project website.
First make a directory for them:
ingex> mkdir ~/rpms
ingex> cd ~/rpms

Now go to http://ingex.sourceforge.net/studio/rpms/ and download the latest versions of these into the new directory (NB: check the names to make sure you get the latest versions, as they have probably been updated since these notes were written):
- codecs-for-ffmpeg-20081009-1.i586.rpm
- ffmpeg-DNxHD-h264-aac-15593-2.i586.rpm
- libodbc++-0.2.4pre3-1.i586.rpm
- shttpd-20070828-1.i586.rpm

Install them with these commands, making sure that you install the codecs-for-ffmpeg rpm first, otherwise the ffmpeg rpm will complain about missing dependencies.
ingex> sudo rpm -i codecs-for-ffmpeg-20081009-1.i586.rpm
ingex> sudo rpm -i ffmpeg-DNxHD-h264-aac-15593-2.i586.rpm
ingex> sudo rpm -i libodbc++-0.2.4pre3-1.i586.rpm
ingex> sudo rpm -i shttpd-20070828-1.i586.rpm

## 3. DVS software installation
If you have DVS cards installed, you should now install the DVS software for them by following the instructions in the later section “DVS card drivers and SDK”.

## 4. AAF software installation
First make a new directory for the source code of the AAF toolkit and move into it. It's best to keep this separate from the Ingex directories, as it's an independent, self-contained, suite of software.
ingex> mkdir ~/AAFtoolkit
ingex> cd ~/AAFtoolkit

Download the AAF-src package by using wget, or if you're not sure of the file details, go to the project website http://sourceforge.net/projects/aaf/ and download the AAF-src package from there (or put the URL from the wget line below into your browser).

ingex> wget http://downloads.sourceforge.net/aaf/AAF-src-1.1.3.tar.gz

Extract the files
ingex> tar xf AAF-src-1.1.3.tar.gz

and make the package
ingex> cd AAF-src-1.1.3
ingex> make install

It's convenient to set an environment variable AAFSDKINSTALL so that we can easily pick-up the AAF installation location later. Use the command here, substituting the installation directory (i.e. the directory where you ran the tar command above), where it says <dir>.

ingex> export AAFSDKINSTALL=<dir>/AAF-src-1.1.3/AAFi686LinuxSDK/g++

As with the earlier environment variables, it's sensible to add this line to your ~/.bashrc file, so the value is always set.

## Final check

You should have added two new 'export' lines in your ~/.bashrc file, i.e.
export DVSSDK=<path to your DVS SDK>
export AAFSDKINSTALL=<path to your AAF SDK>

and with $ACE_ROOT too, those environment variables should now be set. It's sensible to check them before proceeding with the build, which you can do as follows:

First log out, and log back in again to pick up the ACE_ROOT setting, and then type:
ingex> echo $ACE_ROOT

and you should see:
/usr/share/ace

Then check the other two with:
ingex> echo $DVSSDK
ingex> echo $AAFSDKINSTALL

and these should indicate the correct paths to each package, as set earlier in this section.

## Next stages
With the pre-requisites installed, you can now build install the Ingex software from the source code, as described in the section “Building the full system”.
# DVS card drivers and SDK
The current implementation of Ingex works only with DVS capture cards, and so you will need the software for the cards from DVS.
If you do not have the DVS software at this stage then you can test a recorder instead by using the "dvs_dummy" program that will be created in ingex/studio/capture. In that case, skip the instructions here covering the installation of the DVS software and its configuration.
DVS SDKs are available to registered users here:
http://www.dvs.de/products/video-boards/centaurus-ii/login-area/video-boards/sdk.html

Make a directory for the dvs software:
ingex> mkdir ~/dvs
ingex> cd ~/dvs

Using a web browser, download the SDK, e.g. sdk3.2.14.3.tar.gz, into this directory.
The following instructions are based on SDK version 3.2.14.3. If you are using a different version, then modify the directory details, e.g. sdk3.2.14.3, as necessary, for your own setup.
Extract the SDK files from the tar file:
ingex> tar xvf sdk3.2.14.3.tar.gz

Before building the DVS driver, we need to configure the kernel.
We need to do these next commands as root, so su to root:
ingex> sudo su

Change to the directory for your kernel sources. The actual linux directory here will depend on your build, so check in /usr/src to see what's appropriate for your own setup.
root> cd /usr/src/linux-2.6.22.19-0.1
root> make oldconfig
root> make scripts/mod/ #(Note - the trailing slash is important)

Exit the root shell:
root> exit

Now we can make the DVS driver:
ingex> cd ~/dvs/sdk3.2.14.3/linux-x86/driver
ingex> ./driver_create
 < various build messages will appear >
ingex> sudo ./driver_load

If this is successful, you will see messages like these appearing:
- load dvsdriver
- load dvsdriver_sdio
Created device: /dev/iris0 252 0
Created device: /dev/iris1 252 1

(Note that any error about the dvsdriver_sdio driver doesn't matter unless you are using the SDstationOEM boards).
As other parts of the build process will need to access the DVS SDK later, we need to set an environment variable with the path details.
ingex> export DVSSDK=<location of your DVS SDK>
e.g. export DVSSDK=/home/ingex/dvs/sdk3.2.14.3
It is also sensible to put this line into your .bashrc file (i.e. ~/.bashrc), so it's always set.
The DVS driver is now ready.
## Driver loading at boot time
Although the driver can be loaded manually, as above, with the driver_load command, it's convenient for this to be done automatically at boot time. The file dvs_setup deals with this.
Move to the ingex scripts directory:
ingex> cd $workspace/ingex/studio/scripts

Edit the file dvs_setup, using your preferred editor, in this example, vim:
ingex> vim dvs_setup

and change the following line to be the path of the DVS SDK, just installed:
DVS_DIR=/home/ingex/dvs/sdk3.2.14.3

Save the change and close the editor.

You can test the file by using this command
ingex> sudo ./dvs_setup start

There will be a pause, whilst this loads the driver for the cards.
To make this automatic at boot time, follow these steps:
Copy the dvs_setup file to /etc/init.d
ingex> sudo cp dvs_setup /etc/init.d

and make it start at boot time:
ingex> sudo /sbin/chkconfig -a dvs_setup

Note for those running a prior installation of Ingex: the DVS card configuration which was previously also done by dvs_setup, is now carried out when the capture program dvs_sdi is run.

#### Checks
1. You did export DVSSDK didn't you? Check that
ingex> echo $DVSSDK
displays the correct location of the SDK.

2.Check the DVS driver is working with the command
ingex> $DVSSDK/linux-x86/bin/svram info

# Building the full system
You can build all the software in one operation by following the instructions in this section. If you need to build any modules separately, then instead follow the steps in the later section covering that module.
First move to the top level directory containing the Ingex software, i.e.
ingex> cd $workspace/ingex

and run the 'make'...
ingex> make

Build messages will appear during this process, there will probably be some warnings but hopefully no errors.

When the above 'make' has finished, it may be helpful to install two of the executables, as follows: (this will become part of the make process in due course.)

ingex> cd $workspace/ingex/player/ingex_player
ingex> sudo make install

ingex> cd $workspace/ingex/studio/ace-tao/Ingexgui
ingex> sudo make install

The Ingex software is now built but needs to be configured before you can run it. To do this, you should now go through these sections:

- Configuring the Naming Service
- Configuring the database
- UnixODBC installation for C++ client apps
- Configure the web server
- Configure the Controller

Once these are done, you can follow the section “Running the System”, to get everything working.

To use some of the additional features of Ingex, you should subsequently look through the sections:

- Transfer Server (for background copying from recorder to a remote destination)
- Director's Cut (for logging cuts made during recording and creating edits from them)
- Multicasting the video (for distributing the live video feeds from Ingex)

# Configuring the Naming Service

The Naming Service needs to run on one PC in the system so that as each Ingex recorder starts, it can register itself with the Naming Service, and hence becomes available to any controller. You need to configure the Naming Service and enable it as a service to start at boot time as described here.

Remember that you only need to do this on one PC in an Ingex setup.

## Configure the naming service
On the PC that's going to run the Naming Service, using your preferred editor, create the file /etc/sysconfig/TAO-cosnaming, e.g.

ingex> sudo vim /etc/sysconfig/TAO-cosnaming

Put the following line into it:

TAO_COSNAMING_ENDPOINT="-ORBEndPoint iiop://<your IP address>:8888 -ORBDottedDecimalAddresses 1"

where <your IP address> is the IP address of the PC which will run the Naming Service. For example:

TAO_COSNAMING_ENDPOINT="-ORBEndPoint iiop://192.168.1.181:8888 -ORBDottedDecimalAddresses 1"

Rather than using an IP address, you can instead use the hostname at that point, but in that case omit the -ORBDottedDecimalAddresses 1 arguments. Also, to avoid problems later, make sure the DNS entry is correct by pinging the hostname from elsewhere.

If you are using fixed IP addresses, then it's preferable to use the IP address.

If you are running all the Ingex software on the same PC, you can omit the IP address (so the entry reads iiop://:8888) or use 'localhost' as the hostname.

Save the file and close it.

## Enabling the Naming Service

Start YaST and select System, then System Services (runlevel).

Find the entry tao-cosnaming and enable it. Click on Expert and ensure that it is set to start at run levels 3 and 5.

Click on Finish to exit from YaST.

# Configuring the Database

The database is required on only one PC in an Ingex setup. This can be a PC running the Ingex recorder itself, or a separate PC. It is used to store the configurations of the Ingex recorders and also details of the recordings that are made.

## Prerequisites
If you have followed the earlier section “Installation Prerequisites”, you can skip this Prerequisites section.

In YaST, make sure the following are installed:
  unixODBC
  unixODBC-devel
  psqlODBC
  postgresql-server

## Setting up the database
Start the postgres service. As you need to do this as root, first su
ingex> su

then start the database as root
root> /etc/init.d/postgresql start

If this fails to start, then you might want to switch on logging as described in the document
www.postgresql.org/docs/8.1/static/logfile-maintenance.html

Starting postgresql will create an initial database for you in "/var/lib/pgsql/data" - move to that directory (still as root)
root> cd /var/lib/pgsql/data

Next edit the file "pg_hba.conf" (the PostgreSQL Client Authentication Configuration File) and add entries to allow access for the hosts which need to access the database. In this case, we'll allow access from all hosts. First open the file in an editor (in this example, vim)
root> vim pg_hba.conf

Towards the end of the file, below the heading "Put your actual configuration here", you will see these entries

# TYPE DATABASE USER CIDR-ADDRESS METHOD
# "local" is for Unix domain socket connections only
local all all ident sameuser
# IPv4 local connections:
host all all 127.0.0.1/32 ident sameuser
# IPv6 local connections:
host all all ::1/128 ident sameuser

Change the "METHOD" entry for each line from "ident sameuser" to "trust", so the entries now look like this:

# "local" is for Unix domain socket connections only
local all all trust
# IPv4 local connections:
host all all 127.0.0.1/32 trust
# IPv6 local connections:
host all all ::1/128 trust

To allow access to the database from the other PCs in your Ingex system, add the following line but, if necessary, with an appropriate IP address range depending on your network configuration, instead of 192.168.1.0/24 :

host all all 192.168.1.0/24 trust

Save the changes and close file.

Next edit the file "postgresql.conf"
root> vim postgresql.conf

Find the line #listen_addresses = 'localhost' and change this to allow access from the required hosts. Delete the # and change localhost to * to make the line read:

listen_addresses = '*'

Save the changes and close file.

Re-start the postgres service using the command:

root> /etc/init.d/postgresql restart

For convenience, it's best to make the postgres service start at boot time. To do this in YaST:
- start YaST and select System, then System Services (runlevel).
- Find the entry postgresql and enable it.
- Click on Expert and ensure that it is set to start at run levels 3 and 5.

Alternatively, you can use this command:
root> /sbin/chkconfig -a postgresql

Exit the root shell, as the further command are done as the Ingex user
root> exit

## Create the database
Now we create the database that will hold the details of the recorder configurations and also the recordings that are made. In this example, we'll call it "prodautodb".

Remember that, as shorthand, $workspace represents the directory holding the Ingex package from CVS. If you've followed these instructions, it will be /home/ingex/ap-workspace.

Move to the directory containing the setup scripts:
ingex> cd $workspace/ingex/studio/database/scripts

Next run the three scripts that will setup the database user and an initial database and then set a basic configuration for the recorders:

ingex> ./create_bamzooki_user.sh
ingex> ./create_prodautodb.sh
ingex> ./add_basic_config.sh

If anything goes wrong at this point, or you simply want to start again later, you can delete the database with the command:
ingex> ./drop_prodautodb.sh

and then repeat the create_prodautodb.sh and add_basic_config.sh commands above to start with a clean installation of the database.

## Troubleshooting
If you get the error message Ident authentication failed for user "postgres" then check the file /var/lib/pgsql/data/pg_hba.conf which you edited above when setting up the access permissions to the database. The "ident sameuser" entries must be changed to "trust".

The database is now ready. You can check it manually with the psql command:
ingex> psql prodautodb bamzooki

At the prompt prodautodb=> that appears, perform a simple access to the database with this command (don't forget the ; at the end of the command):
prodautodb=> select * from fileformat;

Some (slightly cryptic) file format details should appear showing that the database is working and has relevant entries.

Exit psql with \q or <control-d>:
prodautodb=> \q

# UnixODBC installation for C++ client apps

The recorder accesses a database for its configuration details and also to store details of recordings that are made. In order to access the database (which is described in the section “Configuring the Database”), the UnixODBC software needs to be installed and configured, as described in this section.
You only need to do this on PCs that are running either a recorder or web-server.
## Prerequisites
If you have followed the earlier section “Installation Prerequisites”, you can skip this Prerequisites section.
Open YaST and under Software Management, ensure that these packages are installed:
  libodbc++
  unixODBC
  unixODBC-devel
  psqlODBC (uses libpq.so which is supplied by postgresql-libs rpm)

## Create configuration files
First create the file /etc/unixODBC/odbcinst.ini
ingex> sudo vim /etc/unixODBC/odbcinst.ini

and insert the lines:

[PostgreSQL]
Description = PostgreSQL driver for Linux & Win32
Driver = /usr/lib/unixODBC/libodbcpsql.so
Setup = /usr/lib/unixODBC/libodbcpsqlS.so
FileUsage = 1

Save the file and quit the editor.

Now create the second file /etc/unixODBC/odbc.ini
ingex> sudo vim /etc/unixODBC/odbc.ini

and insert the following contents, substituting the host name or IP address of your own database server, where it shows "*******" in the line "Servername" below:

[ProdAutoDB]
Description = Production automation database
Driver = PostgreSQL
Trace = Yes
TraceFile = sql.log
Database = prodautodb
Servername = ******* <--- your own server details go here
UserName = bamzooki
Password =
Port = 5432
Protocol = 6.4
ReadOnly = No
RowVersioning = No
ShowSystemTables = No
ShowOidColumn = No
FakeOidIndex = No
ConnSettings =

Save the file and quit the editor.

Check the unixODBC configuration by using isql to connect to and query the database:
ingex> isql prodautodb bamzooki bamzooki
SQL> select * from fileformat;

File format details should appear showing that the connection to the database is working correctly.
Exit from isql with quit or <control-d>
SQL> quit

# Configuring the Web server

The web server provides a convenient method of accessing the configuration details for the recorders, monitoring their operation and displaying details of recordings that have been made.

It is probably most convenient to run the web server on the same PC as the Ingex database.
## Prerequisites
If you have already installed the pre-requisite packages as part of a full system build, then you can skip this prerequisites part.

In YaST install the following package:
  perl-DBD-Pg

Whilst in YAST, check that the following packages have already been installed:
  perl-DBI
  apache2
  unixODBC
  unixODBC-devel
  psqlODBC

## Database access
If you have not already done this as part of the Recorder installation on this PC, then you will need to create and edit these two files:
  /etc/unixODBC/odbcinst.ini
  /etc/unixODBC/odbc.ini

For the details required, follow the steps already described under "Database"

## Installation
Move to the directory containing the configuration file for the web software.
ingex> cd $workspace/ingex/studio/web/WebIngex/ingex-config

Edit the configuration file "ingex.conf" to match your system. Make sure your database name and access details are correct in the "database connection settings" section shown below. Note that if your database is not on the same PC as you are now installing the web server, you will need to change the details in the line "db_host" by replacing 'localhost' with the name or IP address of the PC running the Ingex database.

# database connection settings
#
db_odbc_dsn = prodautodb
db_host = localhost
db_name = prodautodb
db_user = bamzooki
db_password = bamzooki

Save the file and exit the editor.

Move up one directory level
ingex> cd ..

and install the files with the command:
ingex> sudo ./install.sh

Note: if you are updating the installation, you can run update.sh instead of install.sh and this will preserve your previous configurations.

Now make the create_aaf (if not already built) and install it by following these steps:

ingex> cd $workspace/ingex/studio/processing/createaaf

If you haven't build the full system already, build the createaaf executable now:
ingex> make

Next create a directory which can be reached by the web server, and copy the executable into it:
ingex> sudo mkdir -p /srv/ingex/createaaf/
ingex> sudo cp create_aaf /srv/ingex/createaaf/

You'll also need to copy a library file there:
ingex> cd $AAFSDKINSTALL/bin/debug
ingex> cp libcom-api.so /srv/ingex/createaaf/

.. and a directory containing two extension library files too:
ingex> cp -r aaftext /srv/ingex/createaaf/

You will now need to edit the configuration file containing the relevant file locations. Do this as follows:

ingex> cd $workspace/ingex/studio/web/WebIngex/ingex-Modules/Material.ingexmodule

Edit the file 'material.conf' and change the contents of the line

avid_aaf_export_dir = ...

to list the directories on your system for the AAF files that will be produced. These are pairs in the form <name>|<destination directory>. Use a relevant name of your choice and a destination directory that's appropriate for your installation. When you select this on the web-page, the AAF file created will be written to the corresponding destination directory, so ensure that it is writeable by the web server (i.e. the user www-run).

## Starting the Apache server
In YaST, go to System -> System Services (RunLevel). Select Apache2 in the list and click on Enable button. You can also check using "Expert Mode" that this will start automatically in run levels 3 and 5.

Click "Finish" to leave the System Services page.

## Testing
Point your web browser at the page http://<your host name>/ingex and you should see the Ingex overview page.

If this doesn't work then open a browser on the same PC as the Apache server, and try http://localhost/ingex to check that the server is running.

If there are still problems, try http://<your host name>/ingex/test and follow the instructions to test your perl, database and web-server setup.

## Configuration Settings
#### Monitoring
With the web server running, you can now configure the monitoring facility within Ingex. However this is not required for initial testing and so this section can be left until later, if preferred.
Open the web interface and click 'configure' in the top right corner to configure the nodes on your network that are to be monitored.
Now specify which machines are to be monitored on your network. For each machine:
- Under Node Configuration, click 'Create New'. Enter the name and IP address (or host name) of the node to add. If the machine is the one running the web server, you can enter 'localhost', although using IP addresses may be more reliable.
- Select the type of machine (Recorder or Filestore) in order to specify which types of information to monitor (e.g. a file server has no capture cards to monitor)
- If you wish to monitor the free space of only some volumes (drives), specify them in a comma separated list, e.g. to monitor the space in /video and /data, you would enter: /video,/data - leaving this box blank will monitor all volumes.
At this stage, as nothing is running, if you go to the 'Status' page, you will be told that monitoring information cannot be displayed. This is because each machine to be monitored must have a program (or multiple programs) running which provide the monitoring data for the web server. As described later, on each recorder machine, you will need to run both nexus_web and system_info_web, and on a file server, just system_info_web. For information on running these, see "Start Monitoring" in the section “Starting additional facilities”.
#### AAF export directories
The Configure web-page also allows you to change the export directories for Avid AAF export, as set above in the AAF file creation section. On the configuration page (under Advanced), choose to edit the material.conf file. Change the line:
avid_aaf_export_dir = '...'
as described in the earlier section.

# Configuring Recorders

You will need to configure the recorder using the web page for Ingex configuration. As installed, this has a basic configuration but you will probably want to make some changes, e.g. recording formats, before use.

Note: a separate document is needed to describe in greater detail how to configure Ingex as there are a large number of options available. The description here is intended to be sufficient to get the system running and perform many of the basic operations.

Start by pointing your browser at:
http://< host name of your web server>/ingex

and click on the Setup tab.

Go to the Recorder page using the link on the left of the screen.

The list of recorders will appear but at this stage there is only one entry - a recorder named “Ingex”. Beneath it is the current configuration for that recorder, in this case “Default”.

Click on the word “Default” and scroll down the page that appears to see the details for that configuration. This initial configuration has four video inputs, each with two audio tracks.

Looking further down within the panel, you will see the encoding settings and other details that will be used, as shown in the two columns on the left here:

Option	Setting	Comment
COPY_COMMAND		Copy cmmand for the recorder to run after a recording has ended. Typically its / /home/ingex/ap-workspace/ingex/studio/processing/media_transfer/xferclient.pl
ENCODE1_BITC	false	true = add burnt-in timecode with encode1
ENCODE1_DEST	/store/mxf_online/	Destination directory for copy command, e.g. directory on remote server
ENCODE1_DIR	/video/mxf_online/	Local destination directory for encode1 files
ENCODE1_RESOLUTION	MJPEG 2:1 (4)	Encoding selected for the encode1 process
ENCODE1_WRAPPING	2	1 = no wrapping; 2 = MXF; 3 = MOV
ENCODE2_BITC	false	true = add burnt-in timecode to encode2
ENCODE2_DEST	/store/mxf_offline/	Destination directory for copy command, e.g. directory on remote server
ENCODE2_DIR	/video/mxf_offline/	Local destination directory for encode2 files
ENCODE2_RESOLUTION	MJPEG 20:1 (8)	Encoding selected for the encode2 process
ENCODE2_WRAPPING	2	1 = no wrapping; 2 = MXF; 3 = MOV
IMAGE_ASPECT	16/9
QUAD_BITC	true	True = add burnt-in timecode to the quad split recording
QUAD_DEST		Destination directory for copy command, e.g. directory on remote server
QUAD_DIR	/video/browse/	Local destination directory for the quad-split recording
QUAD_RESOLUTION	not set (0)
QUAD_WRAPPING	1	1 = no wrapping; 2 = MXF; 3 = MOV
TIMECODE_MODE	1	1 = LTC; 2 = VITC

The encode1 and encode2 resolutions that are available are listed in the table below.

Encoding	Value	Comment	Capture buffer needed
Uncompressed	1
DV25	2		DV25
DV50	3		DV50
MJPEG 2:1	4
MJPEG 3:1	5
MJPEG 10:1	6
MJPEG 15:1S	7
MJPEG 20:1	8
MJPEG 10:1M	9
IMX30	10
IMX40	11
IMX50	12
DNX36p	13	Not yet fully tested; will require dvs_setup to configure the capture cards in the appropriate mode	HD
DNX120p	14	As for DNX36p	HD
DNX185p	15	As for DNX36p	HD
DNX120i	16		HD
DNX185i	17		HD
DMIH264	18	Do not use - not yet ready

In particular, you probably want to check these settings in the recorder's configuration panel:
- encode formats
- BITC on/off for each encode
- Wrapping: none, mxf, mov
- Timecode: LTC or VITC

To change any of the settings, click on the button “Edit” at the top of the panel, just below the bold text “Ingex – Default” (not the Edit button at the top of the page).

After making your changes, click on the button “Done” at the bottom on the panel.

For the settings in the web page that are currently displayed only as a number, you can find the corresponding values in the file $workspace/ingex/studio/databse/src/DatabaseEnums.h, for example:

#define MXF_FILE_FORMAT_TYPE 2
#define LTC_PARAMETER_VALUE 1

There are many other settings that can be made on the web pages but these are the essential ones at this stage. Further documentation will follow on this in due course.

## Capture buffers
If you select an encoding format that requires a different video buffering arrangement, e.g. 4:2:0, you will need to set this on the command line for dvs_sdi. (In time we intend that this will be automatic, but you need to edit the file for now).

To do this, edit the file $workspace/ingex/studio/capture/capture.sh and set the required format after the option -s (which selects the format of the secondary video buffer). For example, for DV25 encoding, make this option DV25, e.g.

sudo nice --10 ./dvs_sdi -c 4 -mc 0 -mt LTC -rt LTC -f YUV422 -s DV25

[Note in passing: if you do not need the secondary buffer, you can save some CPU cycles by omitting the -s option completely.)

dvs_sdi also has additional options (e.g. DLTC and DVITC) which aren't (yet) described here. To see them all type ./dvs_sdi -h at a command prompt.
# Configuring the Controller

## Starting the controller
When it comes to run the controller you will need to use a command like this, but with the IP address of your Nameserver instead of the 192.168.1.181 here:
ingex> ingexgui -ORBDefaultInitRef corbaloc:iiop:192.168.1.181:8888 -ORBDottedDecimalAddresses 1

(Note that for the controller to work correctly, the Nameserver must be running first, but we'll come to that later.)

The file $workspace/ingex/studio/scripts/run_ingexgui.sh runs this command and so it is best to edit this file to use the IP address of your nameserver, and then create a shortcut on the desktop so it can be run easily.

## Replaying files
After a recording has finished, the controller will try to load it into the player so that the files are ready immediately for replay, if required. In this process, the filenames given to the controller have the recorder's hostname prepended to the path, to make it easier when multiple recorders are being used. As an example, if a recorder is running on host “ingexRecorder”, the controller will be looking for the video files beneath the point /ingexRecorder. You will need to have the recorder's video directory at this point otherwise file replay will not work.

If you are running the controller on the same PC as the recorder, you can achieve this by simply having a symbolic as follows:

ingex> sudo mkdir /<hostname of recorder>
ingex> sudo ln -s /video /<hostname of recorder>/video

where /video is the top level directory containing the recordings and <hostname of recorder> is the PC's hostname.

If the recorder is on a separate PC from the controller, you will need to export the recorder's /video directory and mount it on the controller PC. YaST let's you do the export (under Samba Server), then edit the file /etc/fstab on the controller PC, to mount the filesystem locally. For example, add a line like this to /etc/fstab

//192.168.1.181/video /ingexRecorder/video cifs noauto,...etc.,

(the options after noauto will depend on your installation).
In this example 192.168.1.181 is the IP address of the recorder (although you could use its hostname instead at that point), and its hostname is ingexRecorder.
On the controller PC, you can now create the mount point and mount the remote file system with:
ingex> sudo mkdir -p /ingexRecorder/video
ingex> sudo mount /ingexRecorder/video

## Replay via the SDI output
If you want the controller to replay recordings via the SDI output of one of the DVS cards being used for capture, then you must run the controller on the same PC as the recorder, so that it has access to the card.
If you need to control the recorder from a remote PC (i.e. from a studio control room), the easiest way to achieve this is by using a X-session from that PC, to run the Ingex controller application on the recorder itself. In that way the controller has access to the DVS cards, but displays its windows on the remote PC, as required.
You can achieve this with a command on the remote PC such as:
ssh -X ap-workspace/ingex/studio/scripts/run_ingexgui.sh

It's convenient to set up this command as a shortcut on the desktop (and appropriate configuration of ssh means you can avoid it prompting for a password each time it runs).

# Transfer Server

The transfer server looks after the copying of recording from the local discs on the Ingex recorder to a second location, for example, a server or a portable drive plugged into the recorder PC. This means that a second copy of the content is made as soon as possible after a recording has ended, and also makes it possible to delivery the recordings automatically to an edit suite, or other centralised location.

This script is run on each recorder PC and the source and destination directories it uses for the copying are determined by the recorder configuration. It maintains its own configuration file, defined by the constant PATHS_FILE, which allows it to resume interrupted copying when it is started and to avoid copying material repeatedly if the files are removed from the destination directory.
## Prerequisites
PERL modules
IPC::ShareLite
Filesys::DfPortable

To install these see the instructions at www.cpan.org/modules/INSTALL.html but, to summarise, you can either:

a) get each file, then
ingex> tar xvf <module>.tar.gz
ingex>perl Makefile.PL
ingex>make
ingex>make test
ingex>sudo make install

or
b) if you prefer, just run these:

ingex>sudo perl -MCPAN -e 'install IPC::ShareLite'
ingex>sudo perl -MCPAN -e 'install Filesys::DfPortable'

## Building the software
To build the software, move to its directory:
ingex> cd $workspace/ingex/studio/processing/media_transfer

and build the executable cpfs, which performs the copying:
ingex> make

You will see that two perl scripts are in this directory: xferserver.pl and xferclient.pl.

The location of the executable cpfs that you have just built needs to be defined in the file xferserver.pl. Open it in an editor and find the line:

use constant COPY => '/home/ingex/bin/cpfs';

and change /home/ingex/bin/cpfs to the location of cpfs on your system.

Whilst you are editing xferserver.pl you may want to change the value for KEEP_PERIOD from the default week to whatever you require. This is the length of time files are left on the Ingex recorder after being copied successfully to the destination, before the local file is deleted. (This option is to avoid the discs filling too much.)

Another option to consider is the COPY_COMMAND where you can add -p at the end to stop it deleting the files altogether.

# Director's Cut
The Ingex player software can be used in a mode which records cuts made between the video inputs displayed in the quad split presentation. This is the “Director's Cut” facility and allows the video recordings to be made without interruption, but the cuts between them, viewed live in the quad split, are carried through into an AAF file. When this file is opened in a video editor, the video sequence includes the cut which can then be edited if necessary.

The player already includes this functionality so no further installation is required. The usage details for the player will give the command arguments required, but here is an example, which records the cut details into the file /theo/directors_cut.db:

ingex>/usr/local/bin/player --show-tc LTC.0 --audio-lineup -18 --audio-dev 1 --audio-mon 2 --source-aspect 16:9 --quad-split --hide-progress-bar --shm-in 0p --disable-audio --shm-in 1p --shm-in 2p --shm-in 3p --split-select --vswitch-db /theo/directors_cut.db --vswitch-tc LTC.0

It is best to put the command into a script which will ensure that the player starts correctly, if one is already running. See the shell script $workspace/ingex/studio/scripts/directors-quad.sh for an example of how to do this.

To make use of the Director's Cut data in the AAF file that is later created,you will need to set the configuration details in the web-page setup. Refer to the details on the Web Server installation and in particular the section on editing the material.conf file. In that file, find the section:
# the directors cut database files
# format is <name>|<filename>,<name>|<filename> etc.
directors_cut_db = player|/srv/ingex/directors_cut.db

and change the <name>/<filename> pairs on the line 'directors_cut_db' as necessary for your system. This will mean ensuring that the file referred to in the line is the same file as that in the --vswitch-db option shown above in the player command (in that example, /theo/directors_cut.db). You need to make sure that these both refer to the same file. Where the web server is not running on the same PC as the recorder, you will need to arrange access to the file via a network drive, probably from the recorder.

# Multicasting the video

You can set up multicasting from the Ingex recorder PC, so that the incoming video feeds can be viewed over the network using remote players. The streams are MPEG compressed and presented as a standard transport stream, so can be viewed on players such as vlc, mplayer and ffplay.

## Routing details
First you will also need to add some routing details in YaST, as follows:
YaST->Network Services->Routing->Expert Configuration [x]->Add
    dest=224.0.0.0 gw=0.0.0.0 netmask=240.0.0.0

Make sure you select the correct network adaptor, e.g. eth0, - you can confirm the mac address with the command /sbin/ifconfig.

Once the YaST steps are run, you can check the route is in place by running this command and looking for the 224.0.0.0 route:
ingex> /sbin/route -n

## Starting the multicast streams
First move to the capture directory:
ingex> cd $workspace/ingex/studio/capture

Each video channel is multicast separately, using a command like this:
ingex> ./nexus_multicast -c 0 -t -q 239.255.1.1:2000 &

By default this will produce a stream at 3.5 Mb/s with image size 720x576 pixels. You can experiment with the -b and -s options if you want something different. For example,
ingex> ./nexus_multicast -c 0 -t -q -s 360x288 -b 1000 239.255.1.1:2000 &

will produce a ¼ picture at 1 Mb/s.

Further streams can be started by setting the source video channel with the -c option and selecting a different port for the outgoing stream, e.g. to multicast the second video input via port 2001, use this command:
ingex> ./nexus_multicast -c 1 -t -q 239.255.1.1:2001 &

It is easiest to create a script to start the multicast streams as required for your installation. See the file $workspace/ingex/studio/scripts/start_multicast.sh as an example – but note that this will need editing for your configuration.

## Viewing the multicast streams
To view a multicast stream, use one of these players:

vlc udp://@239.255.1.1:2000
mplayer udp://239.255.1.1:2000
ffplay udp://239.255.1.1:2000

[Note: if vlc is not installed, add the videolan repository to YaST (Server: download.videolan.org Directory: /pub/videolan/vlc/SuSE/10.3), and then install vlc.]

## Viewing the uncompressed stream
If you do not use the -t option in the nexus_mulitcast command above, an uncompressed but scaled-down picture will be multicast. Note that the data rate will be about 14 Mb/s for each standard definition source.

It's probably better to use the compressed streams described above, but if you wish to avoid compression, you can use this stream and view it using the Ingex player.

A typical command to produce the stream is:
ingex> ./nexus_multicast -c 0 -q -s 240x192 239.255.1.1:2000 &

Once the player is built, use the command below to start the player and display the streams. Note that in this example, four streams are expected (the -udp-in argument is used four times), so adjust as necessary to match the number of channels that you are streaming. If you try to receive a non-existent stream, the player will wait for it to appear.

ingex> player --pixel-aspect 1:1 --quad-split --prescaled-split --hide-progress-bar --source-aspect 16:9 --udp-in 239.255.1.1:2000 --udp-in 239.255.1.1:2001 --udp-in 239.255.1.1:2002 --udp-in 239.255.1.1:2003

## Troubleshooting
If you are having difficulties getting the multicast streams to work, you can test you network setup by sending a data stream from your Ingex recorder as follows:
ingex> cd $workspace/ingex/common/tools
ingex> ./send_video

Then, on the PCs where you want to receive the stream:
ingex> cd $workspace/ingex/common/tools
ingex> ./receive_video

This will indicate whether the connection has been established, together with packet loss, etc.
# Testing without DVS capture cards
## dvs_dummy
If you do not have the DVS SDK or video capture cards available, the program “dvs_dummy” provides the easiest way of testing the system. It can be run instead of the program “dvs_sdi” and uses the same command line options, but rather than capturing video, it generates colour bars with timecode.
“dvs_dummy” will have been created in the directory $workspace/ingex/studio/capture during the build process.
To run it, move to the capture directory:
ingex> cd $workspace/ingex/studio/capture

and use a command such as this, which will create two dummy inputs:
ingex> ./dvs_dummy -c 2 -m 250

Changing the argument -c 2 to -c 4 will produce four dummy video inputs.

Note: this runs instead of dvs_sdi, so do not run dvs_sdi at the same time.

The remainder of the Ingex system, e.g. recorder, multicast, etc., can now be run in the normal way.

If you want to capture dummy HD frames, first set the DVSDUMMY_PARAM environment variable, e.g.
ingex> export DVSDUMMY_PARAM=video=1920x1080
ingex> ./dvs_dummy -c 2 -m 250

## testgen
As “dvs_dummy” emulates the DVS SDK and capture cards, using it as described above is the preferred method for testing a system if capture cards (or video signals) aren't available. However, a second program “testgen” can also be used, although the only reason for doing this would be if you want to replay a stored video clip rather than using internally generated colour bars.

You will need to build testgen, as follows:
ingex> cd $workspace/ingex/studio/capture
ingex> make testgen

To replay a stored clip, instead of running dvs_dummy, use this command:
ingex> ./testgen -c 4 video.uyvy

You can include an audio file too:
ingex> ./testgen -c 4 video.uyvy audio.wav

To create a suitable video file in uyvy format from an mpeg file, you can use this ffmpeg command line:
ingex> ffmpeg -i video-in.mpg -pix_fmt uyvy422 -f rawvideo video-out.uyvy

# Running the system

The following services should now be run automatically at boot time. These can be checked by looking in YaST -> System -> System Services and checking that they are present and enabled.

- dvs_setup
- Naming_Service
- postgresql
- Apache2

## Start capture
Move to the capture directory
ingex> cd $workspace/ingex/studio/capture

Start the capture process:
ingex> ./capture.sh

As the capture process starts, you will see these messages. If you do not have video connected, this will be reported and if there is a problem with timecode, the screen will fill with messages indicating the timecode discontinuities. Once you correct the timecode feed, the messages will stop.

05 09:47:13.510554 Capturing video as YUV 4:2:2 planar
05 09:47:13.712388 Secondary video buffer is YUV 4:2:0 planar with picture shifted down by one line
05 09:47:13.712405 Master timecode type is LTC using channel 0
05 09:47:13.712417 Using LTC to determine number of frames to recover when video re-aquired
driver version = (3,2,1,0)
05 09:47:13.727347 card 0: device present (720x576)
05 09:47:13.727404 card 0: opened second channel (720x576)
05 09:47:13.727456 card 1: device present (720x576)
05 09:47:13.727512 card 1: opened second channel (720x576)
shmmax=4294967295 (4096.000MiB) probably too big, reducing to 1024MiB
shmmax=1073741824 (1024.000MiB) calculated per channel ring_len=175
element_size=1490432 ring_len=175 (7.00 secs) (total=260825600)
05 09:47:13.730454 chan 0: starting capture thread
05 09:47:13.730503 chan 1: starting capture thread
05 09:47:13.730533 chan 2: starting capture thread
05 09:47:13.730558 chan 3: starting capture thread
05 09:47:13.963867 chan 0: Video signal OK
05 09:47:13.974401 chan 1: Video signal OK
05 09:47:13.989859 chan 2: Video signal OK
05 09:47:13.995984 chan 3: Video signal OK

## Start Quad-split
If you wish, you can now check the incoming video by starting the player in quad split mode, as follows.

Move to the scripts directory:
ingex> cd $workspace/ingex/studio/scripts

Start the player in quad-split mode:
ingex> ./quad-split.sh

Note: if your hardware does not have four video inputs, you will need to modify the quad-split.sh script accordingly. (Reduce the number of –shm-in arguments to match the number of video inputs you have, e.g. for a two-channel system, you only need --shm-in 0p --shm-in 1p in the command line.)

## Start recorder
Move to the recorder directory
ingex> cd $workspace/ingex/studio/ace-tao/Recorder

Look in the file run_recorder.sh; it will contain a recorder command line similar to this:
./Recorder Ingex bamzooki bamzooki -ORBDefaultInitRef corbaloc:iiop:192.168.1.181:8888 -ORBDottedDecimalAddresses 1 $*

Ensure that the corbaloc argument has the IP address of your Naming Service. Here it's 192.168.1.181, but it may be blank in the original version of this file, so put in the appropriate IP address for your configuration.

Start the recorder by running the script
ingex> ./run_recorder.sh

As the recorder starts, it will display the following messages:

Main thread
Recorder name "Ingex"
UpdateSources() loaded config "Default" of recorder "Ingex".
corbaloc:iiop:1.0@192.168.1.181:8888/NameService - object advertised
Recorder running...

Ignore the error about not being able to connect to port 2000. That's a warning because the background copy process xferserver.pl isn't running at the moment.

## Troubleshooting
If you see this message when you start the recorder:

Main thread
Recorder name "Ingex"
UpdateSources() loaded config "10:1m and 2:1" of recorder "Ingex".
corbaloc:iiop:1.0@192.168.1.181:8888/NameService - object could not be advertised
Pausing before re-attempting

it means that the recorder is unable to contact the Naming Service.
Check that:
a) the Naming Service is running. Look in YaST->System->System Services, and to see if the entry tao-cosnaming is running. If it's not, start it now and also set it to start automatically on power-up. If it's not present in the list, check the sub-section “Installing the ACE and TAO packages” in the earlier section “Installation Prerequisites”.
b) the IP address in the script run_recorder.sh corresponds to the PC running the Naming Service.
c) you don't have a firewall enabled between the PCs.

## Start Controller
On the controller PC, move to the directory containing the script that you created when installing the controller, and run it.

For example:
ingex> cd $workspace/ingex/studio/scripts
ingex> ./run_ingexgui.sh

If the recorder is running correctly from the earlier steps, then its name will appear in the “Recorders” list. Click it to select, and timecode display should then start incrementing.

This confirms you have control of the recorder.

## Making a recording
In the controller:

Select the Ingex recorder by clicking on its name in the list at the top

The timecode should be running in the controller display. If it's not, go to recorder configuration web page and check the timecode mode is correct.

Set tape IDs

Click on the “Set tape IDs” button (upper right), and in one of the columns of the grid, enter a sequence of different numbers. At this stage it doesn't matter what numbers are.

Press record

It should turn bright red, indicating that the recorder has gone into record.

Checks:
a) look in the window where you started the capture process – are there any error messages? It shouldn't have changed since you started the capture process itself (unless you interrupted the video or timecode).
b) Look in the window where you started the recorder. You will see messages confirming that the recording has started and the encoding formats being used, but you shouldn't see “Frames waiting” messages (although they're not fatal) or, even worse, “Dropped frames” (which are fatal).

Press stop

If you have followed the controller configuration section, the recordings just made will appear. If they don't, check the setting for the player under “ Player” -> “Player Type” and make sure “Computer screen (accelerated if possible)” is selected.
If this seems correct, then run the controller from a shell prompt and look at the messages that are produced. Initially file not found messages will appear immediately after each recording, but once the files become available, the controller should pick them up for display.
The user documentation covering IngexGUI describes in much more detail how you control Ingex, but we just want to see if it's working at this stage.

Check the recordings

They should have appeared in the appropriate encode directories (initially /video/mxf_online/ and /video/mxf_offline/ ). Copy them over to your preferred editing system and check the content. Success - hopefully!

## Troubleshooting
1. If the recorder drops frames, it may be because you don't have enough CPU power to run two encodings of each video input simultaneously. As a test, go into the recorder configuration web page and turn off one of the encodings by setting either ENCODE1_RESOLUTION or ENCODE2_RESOLUTION to “Not Set”.
2. If it still drops frames, reduce the number of video channels by using the -c option on the dvs_sdi command line in the capture.sh script.
3. Use 'top' or 'gkrellm' to see how much load is on the system. With two quad-core cpus running at 3 GHz, four SD video inputs, with two encodings each, should load the cores to about 50-60%, on average

# Starting Ingex from the Desktop

To make it easier to start the various parts of the Ingex system, you can use the bash script startIngex.sh and stopIngex.sh (in $workspace/ingex/studio/scripts/) to start and stop the required modules, as set beforehand in the file /etc/ingex.conf. This gives a convenient way for users to run the system after power-up, without having to enter the separate commands.
(Note that currently this script will only run under KDE 3.5.)
We'll probably expand the use of /etc/ingex.conf but, at present, its contents is:

# Set the following variables to 1 to enable each facility on startup. Zero means it won't be started.
CAPTURE=1
HD_MODE=0
MULTICAST=0
TRANSFER=0
INGEX_MONITOR=0
SYSTEM_MONITOR=0
QUAD_SPLIT=1

# Recorders listed below. If more than one recorder needs to be started on this PC, then use a space-separated list.
RECORDERS="Ingex"
NAMESERVER="192.168.1.181:8888"

When the bash script $workspace/ingex/studio/scripts/startIngex.sh is run, it will open two terminal windows. In the first, a tab is opened for each of the processes in the upper part of the list which is set to 1. In the second, a tab is opened for each recorder named in the “RECORDERS” variable. In this example, there's only one, but it could be a space-separated list.
To use this facility, go to the scripts directory:
ingex> cd $workspace/ingex/studio/scripts

and edit the file ingex.conf
ingex> vim ingex.conf

Initially you probably don't want to run more than capture, a recorder and possibly the quad-split, in this way, so most lines in this file are already set appropriately.

You will need to change the details for the name server, i.e. change the line:

NAMESERVER="192.168.1.181:8888"
to use the correct IP address of hostname for your system.

You should also check that the name of the recorder in the line:

RECORDERS="Ingex"

matches the name of your recorder (if you've changed it from the default “Ingex”).
If you want Ingex to start in HD mode (currently preset to “1080i”) then set HD_MODE to 1, i.e.
HD_MODE=1

Save the file and quit from the editor.
## Starting Ingex
The startIngex.sh script will look for the file ingex.conf firstly in its current directory, and then in /etc/. This means you can test new setting and then move the ingex.conf file to /etc when it's ready.
To test the settings, type:
ingex> ./startIngex.sh

There will be various pauses, but the two terminal windows will eventually open with the necessary tabs. Check that the required processes are running in them.

If all is correct, you can move ingex.conf to /etc, if you wish.
ingex> sudo mv ingex.conf /etc/

You can now set a shortcut on the desktop to run the startIngex.sh script so that you can start Ingex with one click.

## Stopping Ingex
In the same directory, the script stopIngex.sh can be used to end the Ingex processes and close the terminal windows that were created.
The command is
ingex> ./stopIngex.sh

Again, having a desktop shortcut to run this gives an easy way for the user to shutdown Ingex.

## Troubleshooting
1) If the new terminal windows open but the processes aren't running within them, then make sure that you do not have more that one or two terminal windows open initially. If there are too many open initially, the script can't keep track of them correctly.
2) If the stopIngex.sh script doesn't close the terminal windows, then check that you can write to /tmp as this is where it stores the PIDs of the relevant processes.

# HD Operation

To operate Ingex with HD inputs, you need to set the DVS capture cards in the appropriate mode and then select the required encoding format in the recorder configuration web page.
The configuration of the capture cards is carried out by dvs_sdi, and is set with a command-line option. For example, to operate in “1080i50” mode, the dvs_sdi command line should be:
sudo nice --10 ./dvs_sdi -c 2 -mode 1920x1080i50 -mc 0 -mt LTC -rt LTC -f YUV422
Here the -c 2 option limits the capture to a maximum of two channels, and the -mode option sets the video mode to 1920x1080i50.
To start Ingex in this way, you can use the -h option when you start the capture process with capture.sh. For example:
ingex> cd $workspace/ingex/studio/capture
ingex> ./capture.sh -h

You should see the two channels start in 1920x1080 mode, rather than 720x576.

Refer to the section Starting Ingex from the Desktop for details of how you can set the configuration so that Ingex always starts in this mode.

Finally go to the recorder web page and set the HD encoding format that you require.

Note that at present, you cannot have a secondary encode when running in HD mode. (We're working on it but it's not ready for release yet.)

# Starting additional facilities
## Start monitoring
Optionally, you can also monitor the operation of the Ingex system from a web page. To do this you need to start the monitoring software on each PC for which this is required.

Move to the directory containing the capture software
ingex> cd $workspace/ingex/studio/capture

Start the process that monitors the Ingex capture and recorder operation:
ingex> ./nexus_web

You can also monitor system information about the PC too, by starting this process, in another shell:
ingex> ./sys_info_web

This PC can now be selected for monitoring by selecting the 'Status' tab on the Ingex web page at http://<your Ingex web server>/ingex

## Start transfer server
This stage is optional and only required if you wish to use the background transfer facility to copy recordings to a second destination, e.g. a remote file server.

On the recorder PC run the xferserver script:
ingex> cd $workspace/ingex/studio/processing/media_transfer
ingex> ./xferserver.pl

In the recorder configuration (set via the web page, as above), you will need to set the entry “Copy Command” for the recorder to be:

$workspace/ingex/studio/processing/media_transfer/xferclient.pl

Then, when a recording has ended, the xferclient.pl script will be called to initiate the copy.
## Starting and Stopping Multicasting
To start multicasting streams from the recorder, move to the relevant directory:
ingex> cd $workspace/ingex/studio/capture/nexus_multicast

and start the multicast using the script previously created during your setup of the recorder, i.e.

ingex> ./start_multicast.sh

# Samba shares
Here are some brief notes on setting up SAMBA shares so that an Avid system can access the MXF files directly. (More details may be added later.)

1. Create a structure such as /exports/avid_online/Avid Mediafiles/MXF
   In the MXF directory, make a suitable symbolic link such as HOST.1 -> /video/mxf_online
   where HOST is the host (Avid client) you want to index the files.

2. Install samba and samba-client using YaST (it also installs another two packages as dependencies).

3. In YaST, Network Services-> Samba Server
a) enable at boot up
b) Add /exports/avid_online as an exported filesystem, with name avid_online
c) Do something similar for avid_offline and avid_aaf
d) Export /video as readonly - this is needed by the controller for replay

4. Add samba user ingex:
ingex> sudo su
root> smbpasswd -a ingex
root> exit

5. Check samba export is working, by looking at its status:
ingex> smbstatus

# Building the Recorder

This section describes how to build the Ingex recorder software separately from the full build. If you have already built the full suite by following the section 'Building the full system', you can ignore this section.
These notes are derived from the file $workspace/ingex/studio/docs/RECORDER.txt, which will be updated first when any changes to the instructions are made.
## Prerequisites
If you haven't already, you need to follow the section Installation Prerequisites to install the packages, pre-built RPMs, DVS SDK and AAF toolkit. However, not all the standard packages listed there are required by the recorder - you only need to install these from YaST:
libuuid-devel
libjpeg-devel
libodbc++
unixODBC
unixODBC-devel
psqlODBC (and accept the dependencies that this requires)
Xerces-c
libXerces-c-27
libXerces-c-devel

If you selected the software options suggested in "Installing openSUSE" during installation, then the following packages should already be installed. Install them now if YaST indicates they're not present.
kernel sources
libuuid1
fontconfig-devel
freetype2-devel

## Building the MXF library and Recorder
Build the MXF library and common files:
ingex> cd $workspace/ingex/libMXF
ingex> make

ingex> cd $workspace/ingex/common
ingex> make

Some errors that can occur with this are listed here.
Cannot find -lwritearchivemxf	You haven't built libMXF in the step above
libMXF tests cannot be run without MXFDump	Ignore this as it doesn't matter for this build. (Alternatively you can install the AAFSDK (see its README.txt) if you really need to build this.)
DVSSDK not set and could not be detected	You didn't set the DVSSDK environment variable in DVS driver build instructions above, or you're not using the shell where you set it (it's easiest to put the export DVSSDK line in your ~/.bashrc file so it's always set).

Next make the capture, multicast, monitoring and test software:
ingex> cd $workspace/ingex/studio/capture
ingex> make

You should now have the capture program, "dvs_sdi", multicast server "nexus_multicast", monitoring software “nexus_web” and “sys_info_web”, and the test software "dvs_dummy" in the above directory.

Note that if you do not have the DVS SDK present, the capture software “dvs_sdi” will not have been built during the last 'make'. In this case you can continue and test the full system by running “dvs_dummy” instead of “dvs_sdi”.

Continuing the build, next make the software for handling MXF files.
ingex> cd $workspace/ingex/studio/mxfwriter
ingex> make

Next run the ACE configuration script:
ingex> cd $workspace/ingex/studio/common
ingex> $ACE_ROOT/bin/mwc.pl -type gnuace

Now build the files:
ingex> make

Now build the recorder:
ingex> cd $workspace/ingex/studio/ace-tao
ingex> $ACE_ROOT/bin/mwc.pl -type gnuace

The previous command will produce the following two errors, but these can be ignored:
CIAO_ROOT was used in the configuration file, but was not defined.
DDS_ROOT was used in the configuration file, but was not defined.

ingex> make Recorder-target
ingex> make RecorderClient-target

The Ingex recorder is now built and you should now have the executable:
  $workspace/ingex/studio/ace-tao/Recorder/Recorder

# Building Ingex Player

The player is a versatile piece of software that is extremely useful in the Ingex system. It allows mxf files to be replayed, the incoming video to be displayed during live capture and the multicast streams to be viewed.

This section describes how to build the Ingex player software separately from the full build. If you have already built the full suite by following the section 'Building the full system', you can ignore this section.
These notes are derived from the file $workspace/ingex/player/README.txt, which will be updated first when any changes to the instructions are made.
## Prerequisites
#### 1. Standard packages
If you haven't already installed these, then open YaST and install:
  libuuid1
  libuuid-devel
  portaudio-devel

Also required, but are part of the standard SUSE installation, are these
  freetype (font library)
  portaudio

#### 2. Build and install libraries
If this hasn't already been done, build the libMXF software (you may have done this already as a part of the recorder installation, so it may return immediately, reporting it's up-to-date):
ingex> cd $workspace/ingex/libMXF
ingex> make all

You will also need to make the common library:
ingex> cd $workspace/ingex/common
ingex> make

3. FFmpeg
Note: The player will still compile if you don't have FFmpeg but you will not be able to play files.
If you haven't already installed the FFmpeg rpm then follow the instructions already given in the section "Installation Requisites". You will need to install both the codecs_for_ffmpeg and ffmpeg rpms.

4. DVS SDK
The player will compile successfully if you don't have the DVS SDK, however, you will not be able to replay through the SDI output.
If you haven't already installed the DVS SDK then follow the instructions already given in the section "DVS card drivers and SDK".
Ensure that you have set the DVSSDK environment variable (as explained in the SDK installation steps), so that the build commands below can find the SDK files.

5. Header file nexus-control.h
Normally ingexPlayer will be built within the entire Ingex source tree checked out from CVS and so this note can be ignored. However, if you are building the player separately from rest of the Ingex software, then the header file nexus-control.h is required if replay from shared memory (e.g. the live quad split) and playback through an SDI output is to be included in the build. This file is in $workspace/ingex/studio/capture and it's easiest just to checkout that directory too.

## Installation
With the prerequisites complete, you can build the player:
ingex> cd $workspace/ingex/player/ingex_player
ingex> make

If you are going to build the Ingex GUI software later, then build the C++ library for the player:
ingex> cd $workspace/ingex/player/IngexPlayer
ingex> make

You can test the player with these commands. The first prints the help details, and the second produces a pattern of moving balls.
ingex> ./player -h
ingex> ./player --balls 10

If it's working correctly, install the player, with the following command. (You can safely ignore any error message that reports "no DVS available".)
ingex> sudo make install

# Building IngexGUI
Ingex GUI is the controller for the recorders. You can install this on a recorder PC or, where remote operation is required, for example from a studio control room, on a smaller separate PC, sited elsewhere.

This section describes how to build the Ingex GUI software separately from the full build. If you have already built the full suite by following the section 'Building the full system', you can ignore this section.
These notes are derived from the file $workspace/ingex/studio/ace-tao/Ingexgui/README, which will be updated first when any changes to the instructions are made.
## Prerequisites
1) In YaST, install these packages:
autoconf,
automake
libtool
wxGTK-devel

2) Build the C++ version of the player in $workspace/ingex/player/IngexPlayer/ - for details, see the section “Building Ingex Player”. If the player is built with DVS card support, IngexGUI will be similarly built (and will be able to play back through a DVS card).

3) Install ACE/TAO - see the details in the sub-section “ACE and TAO” in the earlier section “Installation Prerequisites”.

4) Build libidl if you haven't already built another CORBA application, such as the recorder, on this PC. (Remember that $workspace in these command represents the path to the Ingex software, so substitute the full path, if you haven't set the environment variable as suggested earlier.)

ingex> cd $workspace/ingex/studio/ace-tao/IDL
ingex> $ACE_ROOT/bin/mwc.pl -type gnuace
ingex> make

(Don't worry about the CIAO_ROOT and DDS_ROOT warnings.)

## Building Ingex GUI
If you're not sure, check that $ACE_ROOT and $DVSSDK (if player has DVS card support) are defined, by seeing if these commands report sensible locations:

ingex> echo $ACE_ROOT
ingex> echo $DVSSDK

Move to the directory containing the controller software:
ingex> cd $workspace/ingex/studio/ace-tao/Ingexgui

Now run these command to build the software:
ingex> autoreconf
ingex> ./configure
ingex> make

The executable, ingexgui, is built in the sub-directory src.

If the build is successful, install the executable:
ingex> sudo make install

## Troubleshooting
If you see...	Check...
Cannot find -ld3mxfinfo or -lmxfreader	You probably didn't build the libMXF libraries. Check these in the section on building the Player.